## Slide 1
GROOVING MACHINE 02
(Electrical Renewal Project)
Done By
MAINTICS AUTOMATION & ROBOTICS LLP
MAADHAV AUTOMOTIVE
FASTENERS PVT. LTD.
Product Manual

## Slide 2: Table Of Contents
Operation Manual
Electrical Drawing
Troubleshooting Guide
BOM (Bill of Material)

## Slide 3
Operation Manual

## Slide 4: Company Profile Screen
At first when you turn on the Machine this screen will open.
This is the Company Introduction screen.
Click anywhere in the screen to navigate on Main Menu

## Slide 5: 1. MAIN MENU SCREEN
This Screen is for Navigation inside the HMI of below screens.
Below are the list of all available screen in the HMI.
MACHINE MONITOR
DRIVE MONITOR
PART PROGRAM
MACHINE MODE SWITCH
SERVO SETTING
SERVO LOAD ANALYSIS
SERVO ALARM HISTORY
MANUAL OPERATION
INPUT MONITOR
OUTPUT MONITOR
MACHINE ALARMS
VFD ALARMS HISTORY

## Slide 6: 2. PROCESS MONITOR SCREEN
Machine Ready Status
Machine Auto / Manual Mode Status
Machine Auto Running Status
Device Running Status
Home Position Indication and Fault Indication
This screen is to Monitor Whole machine at Single Place
Not Ready
Ready
Manual Mode
Auto Mode
Machine Stopped
Auto Running
Device OFF
Device Running
Not at Home
Machine at Home
Normal
Fault

## Slide 7
6. Total Parts count Cumulative and Cycle time Parts/min.
7. Machine Inputs Monitoring (Cylinder Reed switch)
8. Navigation Bar
This screen is to Monitor Whole machine at Single Place
Here you can monitor all reed switch condition On or Off.
Feed Cylinder
Material Cylinder
Clamp Cylinder
X Axis Cylinder
Y Axis Cylinder
SPINDLE MOTOR STATUS
Used to easily navigate from one screen to another screen
2. PROCESS MONITOR SCREEN

## Slide 8
1. All inputs status from Off to On is as below
This screen is to monitor all PLC Inputs total 16 Nos.
3.INPUT MONITOR SCREEN
INPUT ON
INPUT OFF
MACHINE EMARGENCY PRESSED
MACHINE EMARGENCY NOT PRRESSED

## Slide 9
1. All Output status from Off to On is as below
This screen is to monitor all PLC Outputs total 16Nos.
4. OUTPUT MONITOR SCREEN
OFF
ON

## Slide 10
Alarm screen navigation buttons
Reset button to reset current Alarms
Alarm History Screen access Button
This screen is used to monitor machine current alarms
5. ALARM MONITOR SCREEN

## Slide 11
Alarm screen navigation buttons
This screen is used to monitor machine current alarms
5. ALARM HISTORY SCREEN

## Slide 12
COOLENT PUMP USE
2. COOLENT PUMP NOT USE
3. COUNTER RESET
WITHOUT PART OFF
WITHOUT PART ON
Machine Settings can be done from this screen.
6. MODE SELECT SETTING SCREEN

## Slide 13
Steps for manual operation
  First check Fault Light it should be Off
  Now check Ready Light it should be Green
  Now press Auto Manual selector switch to change mode from Auto to manual
  Now Press Start Button to Start the Device
  It will glow green if device is started.
Manual Operation of all device can be performed using this screen
7. MANUAL OPEARTION 1 SCREEN

## Slide 14
8. PART PROGRAM SCREEN
Here you can change grooving Program
STEP 2WAIT DELAY VALUE 6. STEP 3 SPEED VALUE
OFFSET VALUE
GRONING DATA VALUE
STEP 1 SPEE VALUE
STEP 2 SPEED VALUE

## Slide 15
8. PART PROGRAM SCREEN
Here you can change grooving Program
STEP 2WAIT DELAY VALUE 6. STEP 3 SPEED VALUE
OFFSET VALUE
GRONING DATA VALUE
STEP 1 SPEE VALUE
STEP 2 SPEED VALUE

## Slide 16: SERVO LOAD GRAPH
9. SERVO LOAD SCREEN

## Slide 17
10. SERVO SETTING SCREEN
SERVO MOTOR HOMING STATUS
CURRENT OPSOTION (0.000MM)
CURRENT SPEED (0.000MM/s)
CURRENT TORQUE (0.0%)
SERVO MOTOR JOG SPEED
JOG SPEED MIN MAX
(0.01mm/s) (10.00mm/s)

## Slide 18
11. DRIVE MONITOR SCREEN
DRIVE MONITOR STATUS
Here you can monitor SERVO & VFD STATUS
Here you can change SPINDLE SPEED
MIN MAX
25Hz 60Hz

## Slide 19: Electrical Drawings

## Slide 20: Troubleshooting Guide

## Slide 21
1. HMI ALARM GUIDE

## Slide 22
2. MACHINE AUTO RUNNING FLOW
STOP
START PB
MACHINE HOME
MACHINE AUTO
MACHINE NORMAL
AUTO RUNNING
YES
YES
YES
NO
NO
NO (FAULT)
Check Reed Switch
X20, X22 if NO
Check Manual Screen
If NO
Check Alarm Screen
For any alarm reset alarm before if NO

## Slide 23: BOM (BILL OF MATERIAL)

## Slide 24
1. LIST OF ITEMS USED