## Slide 1
GROOVING MACHINE 02
(Electrical Renewal Project)
Done By
MAINTICS AUTOMATION & ROBOTICS LLP
MAADHAV AUTOMOTIVE
FASTENERS PVT. LTD.
Product Manual

## Slide 2: Table Of Contents
Operation Manual
Electrical Drawing
Troubleshooting Guide
BOM (Bill of Material)
Device Manual/Catalogue

## Slide 3
Operation Manual

## Slide 4: Company Profile Screen
At first when you turn on the Machine this screen will open.
This is the Company Introduction screen.
Click anywhere in the screen to navigate on Main Menu

## Slide 5: MAIN MENU SCREEN
This Screen is for Navigation inside the HMI of below screens.
Below are the list of all available screen in the HMI.
PROCESS MONITOR
DRIVE MONITOR
PART PROGRAM
MACHINE MODE SWITCH
SERVO SETTING
SERVO LOAD ANALYSIS
SERVO ALARM HISTORY
MANUAL OPERATION
INPUT MONITOR
OUTPUT MONITOR
MACHINE ALARMS
VFD ALARMS HISTORY

## Slide 6: 1. PROCESS MONITOR SCREEN
Machine Ready Status
Machine Auto / Manual Mode Status
Machine Auto Running Status
Device Running Status
Home Position Indication and Fault Indication
This screen is to Monitor Whole machine at Single Place
Device OFF
Device Running
Not at Home
Machine at Home
Normal
Machine Fault
1
2
2
2
Sr. No. | Parameter Name | State 0 | State 1 | State 2 | Remarks
1 | Machine Ready | Not Ready | Ready |  | Machine ready status
2 | Manual Mode | Manual Mode | Auto Mode |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 

## Slide 7
This screen is used to Machine Monitor current alarms & Status
1. PROCESS MONITOR SCREEN
6. Servo & VFD Alarm Status
Servo & VFD Alarm ON SERVO & VFD Is Ready to Use
*Counter Reset Button is ON
*Part trial Button is ON
To Reset Part Count, Press this Button for 2second.
This Button used for part trial.
7. COUNTER RESET & PART TRIAL RUN Status
(Machine for run for 1cycle only)

## Slide 8
8. Total Parts count & Cumulative Counter and Cycle time … Parts/min.
9. Machine Inputs Monitoring (Cylinder Reed switch)
10. Navigation Bar
This screen is to Monitor Whole machine at Single Place
Here you can monitor all reed switch condition On or Off.
Feed Cylinder
Material Cylinder
Clamp Cylinder
X Axis Servo position
SPINDLE MOTOR STATUS
(Monitor Running Frequency & Current)
Used to easily navigate from one screen to another screen
1. PROCESS MONITOR SCREEN

## Slide 9
2. DRIVE MONITOR SCREEN
DRIVE MONITOR STATUS:
Here you can monitor SERVO & VFD STATUS.
SERVO:
a) Here you can monitor servo current position.
b) Here you can monitor servo current speed.
c) Here you can monitor servo Current Torque.
VFD:
a) Here you can monitor VFD Frequency.
b) Here you can monitor VFD Voltage.
c) Here you can monitor VFD Current.
d) Here you can monitor VFD Alarm Code.
2. Here you can change SPINDLE SPEED Using Frequency (Hz)
MIN MAX
25Hz 60Hz

## Slide 10
3. PART PROGRAM SCREEN
1. Here you can change grooving Program.
a) DWELL VALUE. * (Here you Can Change Dwell
time in milliseconds )
b) OFFSET VALUE. * (Here you can set Part Offset
Value Press button to get offset value)
c) GROOVING DATA VALUE. * (Here you can set Grooving
Data Value.)
d) FORWARD SPEED VALUE. * (Here you can set Servo
Forward SPEED VALUE.)
e) GROOVING SPEED VALUE. * (Here you can set Servo
Grooving SPEED VALUE.)

## Slide 11
3. PART PROGRAM SCREEN
1. Here you can change grooving Program
f) Reverse SPEED VALUE (Here you can change
Servo Reverse Speed
Value. )
2. Here you can monitor Positioning mode &
Jog mode
a) Here You can Check
POSITION MODE is ON .
b) Here You can Check Jog
MODE is ON .

## Slide 12
COOLENT PUMP ON Condition
2. COOLENT PUMP Off (Bypass) Condition
3. COUNTER RESET BUTTION
WITHOUT Part OFF Condition
WITHOUT Part ON Condition (Machine run without part also)
Machine Settings can be done from this screen.
4. MODE SELECT SETTING SCREEN

## Slide 13
6. OILER DELAY Cycle
* Here you can change Oiler Delay Cycle value.
(After 1000 parts cycle Oiler pump will ON)
7. OILER RUN TIME Sec.
* Here you can change Oiler Run Time Sec.
(After 1000 parts pump ON for 10sec.)
8. COMMULATIVE COUNTER RESET BUTTION
9. AUTO OILER ON Condition (Press this button to run pump manually )
Machine Settings can be done from this screen.
4. MODE SELECT SETTING SCREEN

## Slide 14
Here You can decide the value of current torque ,part detect lower torque and part detect upper torque.
First note down the value of torque when part is available in the machine ,and also note the value of torque when part is not available in the machine. Perform this operation for at least 4 to 5 times. You can observe torque is always greater when part is available with respect to when part is not available in the machine.
Now according to the observation of torque value you can fill the value of
11. PART DETECT LOWER AND PART DETECT UPPER VALUE.
Make sure current torque value (when part is available) is within the range of part detect lower and upper torque value.
Machine Settings can be done from this screen.
4. MODE SELECT SETTING SCREEN

## Slide 15
11. PART DETECT LOWER
* Here You Can Change part Detect Lower Value.
12. PART DETECT UPPER
* Here You Can Change Part Detect Upper Value.
13. Here You Can Check Live SERVO MOTOR TORQUE.
* Make sure current torque(When part is present) is within the range of part detect lower & upper value then it part is counted by counter And if this condition is not
satisfied the part will not count.
Machine Settings can be done from this screen.
4. MODE SELECT SETTING SCREEN

## Slide 16
05. SERVO SETTING SCREEN
1. SERVO MOTOR [JOG SPEED.]
JOG SPEED MIN MAX
(0.01mm/s) (25.00mm/s)
* Here you can enter the Required Password.
Here you can monitor entered Password is correct
. And after homing complete 1cycle Logout Automatically.

## Slide 17
05. SERVO SETTING SCREEN
2. SERVO MOTOR [HOMING MONITORING STATUS]
a) SERVO CURRENT POSITION (-18.000mm)
b) SERVO CURRENT SPEED (0.000mm/s)
c) SERVO CURRENT TORQUE (-1.2%)
a) Here you can enter password by clicking on Login Button, Now Press START HOMING Button for 2 Second and servo will Start homing Automatically (Pass: 12345)
3. SERVO HOMING
* Machine Homing Button OFF.
* Machine Homing is in progress.
* Machine Homing Mode is ON.

## Slide 18
06. SERVO LOAD SCREEN
SERVO LOAD GRAPH
  You Can monitor servo Torque Live Trend.

## Slide 19
This screen is used to monitor machine current alarms
07/12. SERVO+VFD ALARM HISTORY
Alarm screen navigation buttons
Reset button to reset current Alarms
Alarm History Screen access Button

## Slide 20
Steps for manual operation
  First check Fault Light it should be Off(BLACK)
  Now check Ready Light it should be Green
  Now press Auto Manual selector switch(HMI) to change mode from Auto to manual
  Now Press Start Button to Start the Device
  It will glow green if device is started.
Manual Operation of all device can be performed using this screen
08. MANUAL OPEARTION SCREEN

## Slide 21
1. All inputs status from Off to On is as below.
This screen is to monitor all PLC Inputs total 16 Nos.
09. INPUT MONITOR SCREEN
INPUT ON
INPUT OFF
MACHINE EMARGENCY PRESSED
MACHINE EMARGENCY NOT PRRESSED

## Slide 22
1. All Output status from Off to On is as below.
This screen is to monitor all PLC Outputs total 16Nos.
10. OUTPUT MONITOR SCREEN
OFF
ON

## Slide 23
Alarm screen navigation buttons
Reset button to reset current Alarms
Alarm History Screen access Button
This screen is used to monitor machine current alarms
11. MACHINE ALARM MONITOR

## Slide 24: Electrical Drawings

## Slide 25: Troubleshooting Guide

## Slide 26
1. HMI ALARM GUIDE

## Slide 27
1. HMI ALARM GUIDE

## Slide 28
2. MACHINE AUTO RUNNING FLOW
STOP
START PB
MACHINE HOME
MACHINE AUTO
MACHINE NORMAL
AUTO RUNNING
YES
YES
YES
NO
NO
NO (FAULT)
Check Reed Switch &
Slide position
Check Manual Screen
If NO
Check Alarm Screen
For any alarm reset alarm before if NO

## Slide 29: BOM (BILL OF MATERIAL)

## Slide 30
1. LIST OF ITEMS USED