## Slide 1: GROOVING MACHINE 02 MANUAL
Developed By:
MAINTICS AUTOMATION & ROBOTICS LLP
Email : contact@maintics.com
Phone: +91 7042626619
Website : www.maintics.com
Project Description : Grooving Machine 02 Hydraulic to Servo
Customer Name :Maadhav Automotive Fasteners Pvt. Ltd.
Order Number : NA
Order Date :15/03/2024

## Slide 2: GROOVING MACHINE 02 MANUAL
Project Description : Grooving Machine 02 Hydraulic to Servo
Customer Name :Maadhav Automotive Fasteners Pvt. Ltd.
Order Number : NA
Order Date :15/03/2024
© MAINTICS AUTOMATION & ROBOTICS LLP

## Slide 3: Table Of Contents
Operation Manual
Electrical Drawing
Troubleshooting Guide
BOM (Bill of Material)

## Slide 4
Operation Manual

## Slide 5: Company Profile Screen
At first when you turn on the Machine this screen will open.
This is the Company Introduction screen.
Click anywhere in the screen to navigate on Main Menu

## Slide 6: 1. MAIN MENU SCREEN
This Screen is for Navigation inside the HMI of below screens.
Below are the list of all available screen in the HMI.
MACHINE MONITOR
DRIVE MONITOR
PART PROGRAM
MACHINE MODE SWITCH
SERVO SETTING
SERVO LOAD ANALYSIS
SERVO ALARM HISTORY
MANUAL OPERATION
INPUT MONITOR
OUTPUT MONITOR
MACHINE ALARMS
VFD ALARMS HISTORY

## Slide 7: 2. PROCESS MONITOR SCREEN
Machine Ready Status
Machine Auto / Manual Mode Status
Machine Auto Running Status
Device Running Status
Home Position Indication and Fault Indication
This screen is to Monitor Whole machine at Single Place
Not Ready
Ready
Manual Mode
Auto Mode
Machine Stopped
Auto Running
Device OFF
Device Running
Not at Home
Machine at Home
Normal
Fault

## Slide 8
6. Total Parts count Cumulative and Cycle time Parts/min.
7. Machine Inputs Monitoring (Cylinder Reed switch)
8. Navigation Bar
This screen is to Monitor Whole machine at Single Place
Here you can monitor all reed switch condition On or Off.
Feed Cylinder
Material Cylinder
Clamp Cylinder
X Axis Cylinder
Y Axis Cylinder
SPINDLE MOTOR STATUS
Used to easily navigate from one screen to another screen
2. PROCESS MONITOR SCREEN

## Slide 9
This screen is used to Machine Monitor current alarms & Status
2. PROCESS MONITOR SCREEN
1. Servo & VFD Alarm Status
Servo & VFD Alarm ON SERVO & VFD Is Ready to Use
Counter Reset Buttion is ON
Part triali Buttion is ON
Here you can Press PART TRIAL is ON
Here you can Press
PART COUNTER RESET ON
2. COUNTER RESET & PART TRIAL RUN Status

## Slide 10
1. All inputs status from Off to On is as below
This screen is to monitor all PLC Inputs total 16 Nos.
3.INPUT MONITOR SCREEN
INPUT ON
INPUT OFF
MACHINE EMARGENCY PRESSED
MACHINE EMARGENCY NOT PRRESSED

## Slide 11
1. All Output status from Off to On is as below
This screen is to monitor all PLC Outputs total 16Nos.
4. OUTPUT MONITOR SCREEN
OFF
ON

## Slide 12
Alarm screen navigation buttons
Reset button to reset current Alarms
Alarm History Screen access Button
This screen is used to monitor machine current alarms
5. ALARM MONITOR SCREEN

## Slide 13
This screen is used to monitor machine current alarms
5. ALARM HISTORY SCREEN
Alarm screen navigation buttons
Reset button to reset current Alarms
Alarm History Screen access Button

## Slide 14
COOLENT PUMP ON Condition
2. COOLENT PUMP Off Condition
3. COUNTER RESET ON
WITHOUT PART OFF
WITHOUT PART TRIAL ON
Machine Settings can be done from this screen.
6. MODE SELECT SETTING SCREEN

## Slide 15
Steps for manual operation
  First check Fault Light it should be Off
  Now check Ready Light it should be Green
  Now press Auto Manual selector switch to change mode from Auto to manual
  Now Press Start Button to Start the Device
  It will glow green if device is started.
Manual Operation of all device can be performed using this screen
7. MANUAL OPEARTION 1 SCREEN

## Slide 16
8. PART PROGRAM SCREEN
1. Here you can change grooving Program
a) WAIT DELAY VALUE (Here you Can Changr Groving
Data 1sec wait Delay Value.)
b) OFFSET VALUE (Here you can Set Offset
Material Value.)
c) GRONING DATA VALUE (Here you can set Groving
Value.)
d) STEP 1 SPEED VALUE (Here you can set the
step 1 SPEED VALUE)
e) STEP 2 SPEED VALUE (Here you can set the
step 2 SPEED VALUE)

## Slide 17
8. PART PROGRAM SCREEN
1. Here you can change grooving Program
f) STEP 3 SPEED VALUE (Here you can change
step 3 Speed Value )
2. Here you can monitor POSITIONING MODE &
JOG MODE
a) Herer you can monitor
POSITION MOSE is ON
b) Here you can monitor
JOG MODE is ON

## Slide 18
9. SERVO LOAD SCREEN
SERVO LOAD GRAPH
  Here you can monitor servo Load Graphically
  You Can monitor servo Troque Graphically
  c) You Can monitor servo Speed Graphically.

## Slide 19
10. SERVO SETTING SCREEN
1 SERVO MOTOR HOMING STATUS
a) SERVO CURRENT OPSOTION (10.000mm)
b) SERVO CURRENT SPEED (-0.170mm/s)
c) SERVO CURRENT TORQUE (1.1%)
2 SERVO MOTOR JOG SPEED
JOG SPEED MIN MAX
(0.01mm/s) (10.00mm/s)
Here you can enter password and Press 2 Second and servo Start homing Automatically
3 Servo Homing

## Slide 20
11. DRIVE MONITOR SCREEN
DRIVE MONITOR STATUS
Here you can monitor SERVO & VFD STATUS
SERVO
a) Here you can monitor servo current position.
b) Here you can monitor servo current speed.
c) Here you can monitor servo Current Torque.
VFD
a) Here you can monitor VFD Frequency.
b) Here you can monitor VFD Voltage.
c)Here you can monitor VFD Current.
d)Here you can monitor VFD Alarm Code.
2. Here you can change SPINDLE SPEED Using Hz
MIN MAX
25Hz 60Hz

## Slide 21: Electrical Drawings

## Slide 22: Troubleshooting Guide

## Slide 23
1. HMI ALARM GUIDE

## Slide 24
2. MACHINE AUTO RUNNING FLOW
STOP
START PB
MACHINE HOME
MACHINE AUTO
MACHINE NORMAL
AUTO RUNNING
YES
YES
YES
NO
NO
NO (FAULT)
Check Reed Switch
X20, X22 if NO
Check Manual Screen
If NO
Check Alarm Screen
For any alarm reset alarm before if NO

## Slide 25: BOM (BILL OF MATERIAL)

## Slide 26
1. LIST OF ITEMS USED